## Slide 1: Discriminative Scoring for Speaker Recognition Based on I-vectors
Jun Wang
7/07/2014

## Slide 2: outline
Introduction
Background theory
Motivation of NN approach
NN-based discriminative model
Experiments
Conclusions

## Slide 3
Introduction
  Background
    i-vector: the most popular approach to speaker verification. [N. Dehak, 2011]
    PLDA: Probabilistic linear discriminant analysis, achieve state-of-the-art performance.[S. Ioffe, 2006][C. S. Greenberg, 2013]
  Motivation
    limitations of PLDA:
      assumptions on data distributions.
      not directly optimized with respect to speaker verification task.
    the difference between discriminative model and generative model.
  Our approach
    NN-based ( neural-network-based ) discriminative scoring approach.

## Slide 4
Theory background
i-vector[N. Dehak, 2011]
Given a test utterance and an enrollment utterance .
  Speaker verification task is to verify whether and are spoken from the same speaker or different speakers.
  i-vector training and testing.
training corpora
MFCC
MFCC
Baum-Welch statistics
Baum-Welch statistics
UBM
T
Universal background model
Total variability matrix
In training procedure
In testing procedure
UBM
UBM
T
T
Decision method
Mel frequency cepstral coefficient
i-vector

## Slide 5
PLDA [S. J. D. Prince, 2007]
  Probabilistic linear discriminant analysis (PLDA) has been applied successfully to specify a generative model of the i-vector representation, achieves the state-of-the-art performance.
  Technically, assuming a factor analysis (FA) model of the i-vectors of the form:
  is the i-vector, is the mean of training i-vectors, and is a vector of latent factors. The full covariance residual noise term explains the variability not captured through the latent variables.
Speaker dependent part
Session dependent part

## Slide 6
Comparison between generative model and discriminative model
    The generative model and discriminative model are seen as complementary.
 | generative model | discriminative model
1 | modeling observations drawn from a probability density function | do not need to model the distribution of the observed variables
2 | can simulate values of any variable in the model | allows only sampling of the target variables conditional on the observed quantities
3 | can generally express more complex relationships between the observed and target variables. | provides a model only for the target variable conditional on the observed variables
4 | PLDA | NN

## Slide 7
Motivation of NN-based discriminative model
limitations of PLDA
    A disadvantage of PLDA lies in its Gaussian assumption of the prior or conditional distributions on the speaker and session variables, which is not necessarily true in reality.
  prior:
    not directly optimized with respect to speaker verification task.
    We present a NN-based discriminative approach, which does not rely on any artificial assumptions on data distributions.
    The posterior probability that an i-vector pair belongs to the same person are read off from the NN output directly as the trial score.

## Slide 8
    the amplitudes of i-vector also contain speaker information

## Slide 9
NN-based discriminative model
  We presents a discriminative approach which models i-vector pairs using a neural-network ( NN ).
  Suppose and are two total variability factor vectors extracted from test utterance and enrollment utterance respectively.
  Suppose A is projection matrix obtained by LDA (linear discriminant analysis )
  The cosine kernel [A. Hatch, 2006] between and can be written as:
  , corresponding to the i-th dimension of
  , corresponding to the i-th dimension of

## Slide 10
NN structure
how to determine the best N ?
input layer
hidden layer
output layer
from the same speaker
from the different speaker
  $layerdims="--layerdims N+1:200:200:2“.
  $epochs="--epochs 5:5:10“.
  training data: 32500 pairs of utterances, 16250 for same speaker pairs.

## Slide 11
Accuracy on training set
  Different epochs.
  Using all frames for epoch frames, about 32500 frames for each epoch training.
Chart: Accuracy on training set
 | 0.731 | 0.836 | 0.877 | 0.895 | 0.905

## Slide 12
NN testing
input layer
hidden layer
output layer
trial score
  The posterior probability that an i-vector pair belongs to the same person are read off from the NN output directly as the trial score.

## Slide 13
Two combination methods of MLP and PLDA
    c_method 1:
    c_method 2: Use PLDA score as one of the input nodes of NN
input layer
hidden layer
output layer
from the same speaker
from the different speaker

## Slide 14
Experiment
  Database
    Development database
        Fisher English part 1 and 2 as development dataset
        contains 7196 females (12837 utterances).
    We also define a cross-validation dataset
        select 100 speakers from SRE08 to build a cross-validation dataset
        contains about 3000 trials with all 8 common evaluation conditions.

## Slide 15
  Test database
      NIST 2008 speaker recognition evaluation (SRE 2008) [NIST, 2008]:
      core test of SRE 2008 is named short2-short3
      contains 1997 females and 59343 trials.(including the cross-validation dataset)
      at least 2 minutes of speech for a given speaker
      8 common evaluation conditions and define an all trials condition

## Slide 16
Experiments setup
  Configurations of i-vector
      NIST 2008 speaker recognition evaluation (SRE 2008)
      sampling rate of the audio signals is 8 kHz and the sample size is 16 bits
      20-dimensional mel-frequency cepstral coefficients, delta and delta-delta
      2048 Gaussian Mixtures
      400 total factors
      150-dimensional LDA, 400-dimensional PLDA
  MLP setup
      2 hidden layers with 200 nodes
      Output layer: 2 nodes, 1 0 for the same speakers, 0 1 for the imposters
      training data: 32500 pairs of speakers
      epoch frames: using all training data in each epoch
      input layer: number of nodes dependents on the number of LDA dimensions we choose

## Slide 17: Experiment results
  NN test on the cross-validation dataset
    N=10 will get the best result

## Slide 18
  NN test under different conditions

## Slide 19
  NN test on all trials

## Slide 20
  NN test with different input dimensions (from N=1 to N=20)

## Slide 21
  Combine PLDA and NN

## Slide 22: Experiment results
EER% | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9
LDA | 24.07 | 1.49 | 24.18 | 14.56 | 14.54 | 10.25 | 6.46 | 6.58 | 1.46
PLDA | 19.50 | 2.18 | 19.71 | 14.54 | 11.22 | 8.06 | 4.27 | 4.46 | 17.22
NN | 18.23 | 0.93 | 18.82 | 15.65 | 14.63 | 8.70 | 5.07 | 4.46 | 15.56
c_method1 | 17.57 | 0.93 | 17.82 | 13.26 | 12.07 | 7.77 | 4.40 | 4.18 | 15.47
c_method2 | 17.69 | 0.93 | 18.09 | 12.94 | 12.20 | 7.89 | 4.27 | 4.18 | 15.74

## Slide 23
[1] N. Dehak, P. Kenny, R. Dehak, et al. Front-end factor analysis for speaker verification[J]. Audio, Speech, and Language Processing, IEEE Transactions on, 2011, 19(4): 788-798.
[2] P. Kenny, G. Boulianne, and P. Dumouchel, “Eigenvoice modeling with sparse training data,” IEEE Transactions on Speech and Audio Processing, vol. 13, no. 3, pp. 345–354, 2005.
[3] A. Hatch and A. Stolcke, “Generalized linear kernels for one-versus-all classification: application to speaker recognition,” in to appear in proc. of ICASSP, Toulouse, France, 2006.
[4] A. Hatch, S. Kajarekar, and A. Stolcke, “Within-class covariance normalization for SVM-based speaker recognition,” in Proc. Int. Conf. Spoken Lang. Process., Pittsburgh, PA, Sep. 2006.
[5] S. J. Prince and J. H. Elder, “Probabilistic linear discriminant analysis for inferences about identity,” in International Conference on Computer Vision. IEEE, 2007, pp. 1–8.
[6] The NIST Year 2008 Speaker Recognition Evaluation Plan, http://www.nist.gov/speech/tests/spk/2008/sre-08_evalplan-v9.pdf.
[7] P. Kenny, G. Boulianne, P. Ouellet, and P. Dumouchel, “Joint factor analysis versus eigenchannels in speaker recognition,” IEEE Transactions on Audio, Speech, and Language Processing, vol. 15, no. 4, pp. 1435–1447, 2007.
[8] A. O. Hatch, S. S. Kajarekar, and A. Stolcke, “Within-class covariance normalization for SVM-based speaker recognition.” in INTERSPEECH’06, 2006.
[9] A. Solomonoff, C. Quillen, and W. M. Campbell, “Channel compensation for SVM speaker recognition,” in Proc Odyssey, Speaker Language Recognition Workshop 2004, 2004, pp. 57–62.
[10] S. Ioffe, “Probabilistic linear discriminant analysis,” in ECCV 2006, 2006, pp. 531–542.
[11] M. McLaren and D. V. Leeuwen, “Source-normalised-and-weighted LDA for robust speaker recognition using i-vectors,” IEEE Transactions on Audio, Speech, and Language Processing, pp. 5456–5459, 2011.
[12] N. Dehak, R. Dehak, P. Kenny, P. Ouellet, and P. Dumouchel, “Support vector machines versus fast scoring in the low-dimensional total variability space for speaker verification,” in International Conference on Spoken Language Processing - ICSLP. IEEE, 2009, pp. 1559–1562.
[13] C. S. Greenberg, V. M. Stanford, A. F. Martin, M. Yadagiri, G. R. Doddington, J. J. Godfrey, and J. Hernandez-Cordero, “The 2012 NIST speaker recognition evaluation,” 2013.
References

## Slide 24: THANKS